## Slide 1: CAPSTONE PROJECT
VRRP BASED FAILOVER ROUTING SYSTEM PRESENTED BY: Prashanth (192524072) Arshad (192525060) Kamali (192512093)

## Slide 2: LIST OF CONTENTS Abstract Introduction to VRRP Need for Failover Routing VRRP Architecture VRRP Configuration Priority & Preemption VRRP Packet Flow Implementation (Packet Tracer) Result & Outcome Conclusion

## Slide 3: ABSTRACT VRRP (Virtual Router Redundancy Protocol) ensures continuous network availability. Provides automatic router failover in LANs. Elects a Master and Backup routers for default gateway handling. Ensures no disruption in network communication during router failure.

## Slide 4: INTRODUCTION TO VRRP Defined in RFC 5798. Enables creation of a virtual router IP shared among multiple routers. Master handles traffic; Backup takes over if Master fails. VRRP provides seamless gateway redundancy.

## Slide 5: NEED FOR FAILOVER ROUTING Prevents single-point gateway failure. Increases network uptime and reliability. Reduces manual recovery efforts. Ideal for mission-critical network services. Maintains smooth network operation during faults.

## Slide 6: How VRRP Works (Failover Routing) Multiple routers are grouped together in a VRRP setup. They share a Virtual IP address — this is the IP your devices use as the default gateway. One router becomes the Master and handles all traffic. The others are in Backup mode, just waiting. All routers send VRRP hello messages to each other. If the Master stops responding (fails), the Backup with the highest priority becomes the new Master.

## Slide 7: VRRP ARCHITECTURE Virtual IP assigned to a group of routers. One router becomes Master (active), others are Backup (standby). Master sends periodic advertisements to Backups. If advertisements stop, Backup takes over. Failover is automatic

## Slide 8: VRRP CONFIGURATION Set a common virtual IP for all routers. Assign priority (higher value = more preferred). Enable preemption to allow takeover by higher priority router. Monitor interface states to update router status. Configure using tools like Packet Tracer or GNS3.

## Slide 9: PRIORITY & PREEMPTION Priority range: 0 to 255 (default: 100). Highest-priority router becomes Master. Preemption: Ensures high-priority router can reclaim Master role. Priority 0: Router cannot be elected Master. Interface tracking helps dynamically adjust priority.

## Slide 10: RESULT & OUTCOME Packet Tracer simulation with 2 routers. When Master goes down, Backup router takes over instantly. No disruption in network traffic. System reverts to original Master when restored. Achieved failover within 3 seconds.

## Slide 11: CONCLUSION VRRP enhances network fault tolerance. Provides automatic and fast gateway redundancy. Suitable for enterprise and high-availability systems. Easy to set up using simulation tools.